## Slide 1: 1. Given address 192.168.2.68/24 A. Find the network address 192.168.2.0 B. Find the first and last usable address 192.168.2.1 and .254 C. Find the broadcast address 192.168.2.255

## Slide 2: 2. You are a network administrator for an enterprise that needs to create at least 3 subnets. The company has chosen the private address 192.168.0.0/24 as its internal network address. Your task is to design the subnets and provide detailed information for each one. A. How many subnets can be created? B. For each subnet, provide the following details: Network address Host address range Broadcast address Subnet mask

## Slide 3: Answer 2
How many subnet can we create?
`we have address of 192.168.0.0 /24 as our network
So we use the formula 2^n
In /24 we have 8 bits
To create 3 subnet we have to borrow 2 bits from our host network
So now our host network is /26
2^2 = 4 (number of subnet)
2^6 = 62, 62 – 2 = 60 (number of host per subnet)
B. Provide details
_ subnet 1
network address : 192.168.0.0
Host address : 192.168.0.1 and .62
Broadcast network : 192.168.0.63
subnet mask : 255.255.255.192
_ subnet 2
network address : 192.168.0.64
Host address : 192.198.0.65 and .126
Broadcast network : 192.168.0.127
subnet mask : 255.255.255.192
_ subnet 3
network address : 192.168.0.128
Host address : 192.168.0.129 and 190
Broadcast network : 192.168.0.191
subnet mask : 255.255.255.192
_ subnet 4
network address : 192.168.0.192
Host address : 192.168.0.193 and 254
Broadcast network : 192.168.0.255
subnet mask : 255.255.255.192

## Slide 4: 3. You are a network administrator for an enterprise company that has six departments. Each department has specific requirements for the number of host devices they need to accommodate. Your task is to use Variable Length Subnet Masking (VLSM) to allocate subnets within the provided private IP address range to meet the needs of each department. The provided IP address range is 192.168.10.0/24. Department Requirements: Sales: 50 host devices, Management: 5 host devices, HR: 4 host devices, Admin & Finance: 12 host devices, Marketing: 42 host devices, IT: 10 host devices A. Calculate the subnet sizes B. Allocate the subnets for each department C. Document the IP address range

## Slide 5
3.
A, calculate the subnet size
Sale = 50 host devices 2^6 = 64
Management = 5 host devices 2^3 = 8
HR = 4 hosts 2^2 = 4
Admin & finance = 12 hosts 2^4 = 16
Marketing = 42 hosts 2^6 = 64
IT = 10 hosts 2^4 = 16

## Slide 6: 4. You are managing an ISP network using the IP address range 172.30.0.0/16. Your task is to create smaller subnets that can each support a minimum of 800 host addresses. A. How many subnets can you create from the given network with at least 800 host addresses each? B. Determine the 957th host address within the 25th subnet.

## Slide 7
4, IP range 172.30.0.0/16, create smaller subnet that can store 800 hosts minimum
A, how many subnet can we create
In /16 we have 16 bits of host bit
So to create a smaller subnet we need to borrow 6 bits from the host portion
Now the host portion is /22 which is 10 bits that can store 2^10 = 1024 – 2 = 1022 hosts > 800
Formula for the subnet is 2^subnet bit, 2^6 = 64 subnet- network.
B, find the 957th host’s IP in the 25th subnet network
Subnet 1; 172.30.0.0
Subnet 25, 172.30.(25 - 1)* 4.0 = 170.30.96.0/ 22
the 1th host of this subnet is 170.30.96.1
the 957th host of this subnet is 170.30.99.189
The solution is
one subnet can have 256 hosts so we take 957 / 256 we got 3.7 so we have 3 of 256 and 256 + 256 + 256 + 189 = 957